Hexapod_v2 package format

motor	cmd	value least significant byte	...	value most significant byte
1 byte	1 byte	1 byte	...	1 byte

Table 1. Interconnection between desktop program and MCU (Hexapod_v2).

cmd	Name	Destination (MCU)	Description	Parameters			Number of bits in the value
				motor	first byte	other bytes
0	HEXAPOD_POS	from	Current motor position	id	Position		2
1	HEXAPOD_SPEED	from	Current motor speed	id	Speed		2
2	HEXAPOD_ERR	from	Last motor error	id	Error code		1
3	HEXAPOD_START	to	Start a move	0	Specifies a move mode: / ???		1
4	HEXAPOD_STOP	to	Stop a move	0	0		1
5	HEXAPOD_FREQUENCY	to	Frequency in the oscillation mode	0	Frequency		2
6	HEXAPOD_SPEED_TO	to	Speed in the oscillation mode	0	Speed		2
7	HEXAPOD_START_POS	to	Start position in the oscillation mode	0	Start position		2
8	HEXAPOD_MODE	to	Mode in the oscillation mode	0	Mode (roll, pitch)		1
9	HEXAPOD_SIZE	to	Script size in the script mode	0	Script size		2
10	HEXAPOD_VALUE	to	Script item in the script mode	0	Script item		2
11	HEXAPOD_REINIT	to	Re initialization of motors	0	0		1
12	HEXAPOD_ANSWER	from	Answer on the command	0	HEXAPOD_START – hexapod has started / HEXAPOD_STOP – hexapod has stoped / HEXAPOD_FREQUENCY – frequency has set	HEXAPOD_START – 0 / HEXAPOD_STOP – 0 / HEXAPOD_FREQUENCY – frequency / HEXAPOD_SPEED_TO – speed / HEXAPOD_START_POS – start position	3

Table 2. Interconnection between stateChanged signal (Dsrv_Hexapod_v2 class) and onStateChanged slot (Widget class).

cmd	Name	Description	Parameters
			motor	value (always 32 bits)
0	HEXAPOD_POS	Current motor position	id	Position
1	HEXAPOD_SPEED	Current motor speed	id	Speed
2	HEXAPOD_ERR	Last motor error	id	Error code
12	HEXAPOD_ANSWER	Answer on the command	0	HEXAPOD_START (*) – hexapod start command was accepted / HEXAPOD_STOP (*) – hexapod stop command was accepted / HEXAPOD_FREQUENCY (*) – frequency / HEXAPOD_SPEED_TO (*) – speed_to / HEXAPOD_START_POS (*) – start position / HEXAPOD_MODE (*) – mode in the oscillation mode / (*) – see Table 1
100	HEXAPOD_ERR_USART_OPEN	USART device did not open	0	0
101	HEXAPOD_ERR_USART_IO	Read/write with USART device led to error	0	0 – read / 1 – write
102	HEXAPOD_DEV_OPENED	Device was opened	0	0
103	HEXAPOD_DEV_CLOSED	Device awas closed	0	0
104	HEXAPOD_ERR_USART_CLOSE	USART device did not close	0	0

Table 3. Interconnection between sendCommand signal (Widget class) and onSendCommand slot (Dsrv_Hexapod_v2 class).

cmd	Name	Description	Parameters
			data	size
200	HEXAPOD_CMD_CON	Try to open a device	nullptr	0
201	HEXAPOD_CMD_DISCON	Try to close a device	true – need a HEXAPOD_ST_CLOSED answer on stateChanged signal (see Table 2) / false – answer does not need	1
202	HEXAPOD_CMD_SEND	Send a packet	Pointer to the data	Packet size